SCICEX-99

## TECHNICAL ADVISOR’S LOG

- Introduction.  SCICEX-99 was conducted aboard USS HAWKBILL (SSN 666) during March-May 1999.  The following report describes the activities which took place during the data collection portion of SCICEX-99 (0230 on 2 Apr to 1830 on 14 May).  It is intended as a resource for investigators to use in understanding the sequence, rationale, and context of our data collection effort.

- Schedule.  The overall science program which was agreed to at the planning meeting was laid out in the Science Test Plan (STP).  I will summarize our intentions phase-by-phase as we go along and point out those times that we have deviated significantly from our plan (and why).  The STP also allowed 1 day contingency time for unplanned delays, ship’s surfacings, repeat probe launches, etc. and another ½ day for Chief Scientist contingency time.  I will point out those times that significant portions of this pool were used.

- Equipment.

- The following hardware was installed/carried to assist in the data collection:

- Digital Ice Profiling System (DIPS III).  Run continuously while submerged to digitize and record ice draft data from the ship’s high frequency, upward-looking sonar (topsounder).

- Sidescan Sonar.  Run continuously when submerged to provide qualitative swath view of the underside of the ice to assist the submarine in identifying potential surfacing sites.  There was no request or requirement to record this data so no recordings were made.  However, it was used to monitor overhead conditions during the data collection period.

- Submarine Remote Video System (SRVS).  Operated continuously when submerged to assist the submarine in evaluating potential surfacing sites.  As with sidescan, we had no requirements to record this data.  Recordings were made for media personnel.

- ICECAT CTDs.  SBE-19s mounted in the submarine’s sail and run continuously while submerged.  Two independent systems were provided, #1 with a fluorometer attached, #2 with a transmissometer attached, and both with Dissolved Oxygen (DO) sensors attached.  Because of susceptibility of the DO sensors to damage from cold air temperatures, they were not installed until the submarine’s third surfacing at the ice camp (11 Apr).

- Acoustic Doppler Current Profiler (ADCP).  Mounted on the bow of the submarine with its beams directed upward toward the ice.  Operated continuously while submerged.

- Sub-Bottom Profiler & Swath Mapper.  The two acoustic components of SCAMP, mounted on the keel with control/readout in the Torpedo Room.  Operated continuously while submerged.

- Gravimeter.  A BGM-3 system mounted in the Torpedo Room and co-recorded with SCAMP Data on the DACQS system.  Operated continuously.

- Performance.  No known problems existed at the start of data collection.  Problems which developed later are discussed below in the narrative at the time they occured.

- Science Team.

- The following civilians are embarked as the Science Team:

Dr. Margo Edwards (University of Hawaii) – Chief Scientist

Dr. Bernie Coakley (Tulane University) – Acting Chief Scientist in Dr. Edward’s absence

Dr. Terry Whitledge (University of Alaska, Fairbanks)

Dr. Dean Stockwell (University of Alaska, Fairbanks)

Dr. Steve Okkonen (University of Alaska, Fairbanks)

Dale Chayes (LDEO)

Mark Rognstat (University of Hawaii)

Randy Ray (ASL)

Myself

- The presence of an ice camp north of Alaska allowed us to customize the science team for different phases of the operation.  The riders embarked during various times are:

- Terms of Reference.  The following conventions were used in this log and its companion, the Ship’s Operation Log.

- Ship’s Depth is given as the depth of the ship’s keel, in feet.  The on-board water sample port is 8 feet shallower and the ICECAT sensors 50 feet shallower than this depth.

- At various times, the ship operated in two different coordinate systems – either the standard geographic coordinate system or, for 3 periods of time, the transverse coordinate system.  When in transverse, ship’s headings will be given in transverse coordinates. These may be corrected to geographic by adding east or subtracting west geographic longitude but the result is valid only until another longitude line is crossed.  All other references, such as position and “big picture” stuff (e.g., going north toward the North Pole) will remain in geographic.  The periods of transverse operation are:

- During the most northerly extent of the Phase 2 Chukchi Cap Survey (0037-1628 on 6 Apr).

- During the most easterly extent of the Phase 4 Alaska Shelf Survey (0628 on 14 Apr to 0324 on 15 Apr)

- During the high latitude periods of operation (from last APLIS surfacing on 16 Apr to final surfacing on 14 May).

- Speed will be in knots.

- Time/date on these logs and for all records is in Zulu.

- Definitions.  Several terms are used to describe our activities which may not be clear to the reader.  I’ve tried to anticipate these and provided clarification below.

- Housekeeping (H/K).  Routine boat activities which temporarily take precedence over scientific data collection.  This normally would take place once daily and include receipt of communications, discharge of ship’s tanks, and launching of routine XCTDs.  During our transit to the Arctic, we had recurring problems with the toilets clogging so the boat instituted a policy of using more water to flush.  As a result, the sanitary tank filled much more quickly than usual requiring more frequent excursions to shallow depths to blow this tank.  Normally, this resulted in two brief housekeeping trips per day in addition to the normal, full-up daily housekeeping period.

- Spiral or Submerged Hydrocast.  In order to collect samples in a roughly vertical profile, the submarine will spiral to selected depths while collecting water samples.  This is done in such a way as to keep the submarine within a circle about 300 yards in diameter.

- Normally, we will do a spiral in conjunction with the daily housekeeping at the “standard” depths of 190, 440, and 750 feet.  Where the bottom will not allow the 750 foot sample, we will to a 2-depth spiral.

- More detailed vertical sampling will be conducted at 24 specified locations while spiraling to more (typically 8) depths.

# In-line samples will be collected as the boat continues on the designated track without slowing down.  In these cases, the position given for this sample is the ship’s location at the time the sample was started.

# 2 April 1999

| 0230 | Entered the Data Release Area and commenced data collection. Energized all data systems. The original plan had us proceed directly to the camp to arrive pre-dawn local (1100Z) on the 4th. The boat has done so well getting through the Bering Strait that we’re 41 hours ahead of schedule. If we went straight to the camp, they may not be ready for us (post-facto comment: this assumption was true) so we’ll do some science along the way. The first and last legs of the planned Phase 2 Chukchi Cap survey are nearby so we’ll try to get them done early. To do so, we’ll do the following: Take a few hours to transit from the entry point (74-30N/170-50W) to Point 1-1 (74-45N/167-30W) while we ensure that all the systems are operating properly. At Point 1-1, we’ll do a 2-depth spiral. From Point 1-1, we’ll do a SCAMP leg at 200ft/8kts to Point 1-2 (73-56N/160-57W). For most of the latter half of this transit, we’ll roughly follow the 200fm curve allowing us to look both up- and down-slope for iceberg scars. We’ll also take a few in-line samples along the way. From Point 1-2, we’ll divert to the north to pass over a core site at Point 1-3 (76-15.22N/160-35.38W). Once past that point, we’ll do a 3-depth spiral then go deep and proceed directly to the camp. Having done all of this, we still expect to arrive at the camp about 24 hours early. We’ll rendezvous during the pre-dawn hours tomorrow then surface at first light. |
| --- | --- |
| 0350 | Came shallow for housekeeping. Since this leg to Point 1-1 is being used primarily for equipment checkout, we won’t bother trying to preserve track continuity. |
| 0441 | Resumed direct transit to Point 1-1. We’ll interrupt again to complete housekeeping in about a half hour. |
| 0511 | Circling to conduct housekeeping. |
| 0536 | Housekeeping complete. Proceeding to Point 1-1. |
| 0738 | Reached Point 1-1. Commenced 2-depth spiral (Event #1). |
| 0920 | Completed sampling. Commenced survey track to Point 1-2. We will use 200ft/8kts which is the standard survey depth/speed for Phase 2. We’ll do 2 in-line samples along the way and a third at Point 1-2. |
| 1410 | Commenced in-line sample (Event #2). |
| 1946 | Commenced in-line sample (Event #3). |

# 3 April 1999

| 0057 | Approaching Point 1-2. We’ll do an in-line sample through the turn. Commenced in-line sample (Event #4). |
| --- | --- |
| 0102 | At Point 1-2. Commenced transit toward Point 1-3. |
| 0345 | Passed Point 1-3. We’ll go a couple miles past then conduct our first 3-depth spiral and daily housekeeping. |
| 0400 | About 2nm past Point 1-3. Commencing circling for 3-depth spiral. |
| 0404 | Launched XCTD #1 (Event #5). |
| 0411 | Commenced 3-depth sampling (also Event #5). |
| 0524 | Completed sampling. Commenced housekeeping. |
| 0716 | Completed housekeeping. Commenced transit to the ice camp. We’re not in too big a rush to get there because we can’t surface until it’s light (about 10 hours from now). |
| 1100 | Approaching the ice camp. We’ll be selectively securing data systems as we approach in order to avoid interference with systems needed to support rendezvous and surfacing. |
| 1732 | In position beneath feature designated by the camp. Commenced ascent. |
| 1738 | Surfaced. While surfaced, we’ll embark Dr. Edwards. |
| 2305 | Submerged. |
| 2342 | Commenced Phase 2 – Chukchi Borderland Survey. This is heavily modified from the Science Test Plan to take into account the tracks we ran during Phase 1, the extra time resulting from our early arrival, and recent changes in priorities by the PIs. We’ll initially transit to the Northwind escarpment at 750ft/16 kts, then survey the Chukchi Cap at 200ft/8kts. This will consist of 2½ legs oriented roughly N-S. From there, we’ll go to 440ft/12kts, transit back east to the Northwind Rise, and conduct a survey in the shallow region of the Northwind Rise. From there. We’ll go back to 750ft/16 kts to return to the camp on 10 April. With all of these changes, the Science Test Plan has become irrelevant so I won’t try to refer to track points by number. As far as water sampling, we’ll do 2- or 3-depth spirals with the daily housekeeping events. In addition, we have six in-line samples budgeted. Dr. Okkonen has elected to concentrate these during our shallow operations above the Chukchi Cap. |

# 4 April 1999

| 0007 | Going deep and fast to transit to the start point of our survey. |
| --- | --- |
| 0344 | Reached the Northwind Rise. Came to 200ft/8kts. Our next leg will take us westward across the base of the Chukchi Cap. This is intended to parallel or Phase 1 survey leg, offset one swath (about 5nm) northward. |
| 1837 | Reached the westernmost extent of this leg. Turning north toward the tip of the Chukchi Cap. |
| 2339 | Broke track for daily housekeeping and 2-depth spiral. We’ll do housekeeping first then return to the track to do the science. |

# 5 April 1999

| 0035 | Completed housekeeping. Returning to the point at which we broke from track. |
| --- | --- |
| 0105 | Launched XCTD #2 (Event #6) – sat. |
| 0115 | Commenced 2-depth spiral (also Event #6) |
| 0203 | Completed sampling. |
| 0209 | Resumed survey. |
| 0457 | Slowed from 8 kts to 3 kts to obtain a neutral trim. We’ll do this about once every 6 hours while operating at 200 ft in really shallow water. They’ll show up on the Ops Log but I won’t identify them in this narrative. |
| 0510 | Resumed 8 kts. |
| 0645 | Commenced in-line sample (Event #7). |
| 1020 | Commenced in-line sample (Event #8). |
| 1400 | Commenced in-line sample (Event #9). |
| 1931 | Commenced in-line sample (Event #10). |

# 6 April 1999

| 0037 | Shifted heading reference to transverse coordinate system. |
| --- | --- |
| 0118 | Commenced in-line water samples (Event #11). |
| 0357 | Broke track for housekeeping and spiral. |
| 0400 | Launched XCTD #3 (Event #12). Sat. |
| 0406 | Commenced 3-depth sampling (also Event #12). |
| 0514 | Completed sampling. Proceeding with housekeeping. |
| 0609 | Completed housekeeping. Resuming survey. We’ve made 2 changes to the remainder of this portion of the survey. First, we’re going to extend the endpoint of this northbound leg as far north as necessary to ensure we’re over the abyssal plain before we turn. Secondly, we’ve moved the remaining legs in this north-south Chukchi Cap survey to the west to reduce line spacing. Originally, we had 5nm spacing but, since SCAMP swath is only 4km in this shallow water, 5nm spacing would not allow sufficient overlap. So we’re tightening things up to 3nm spacing. Proceeding northward. |
| 0930 | In >1600fms of water. Terminating the first Chukchi Cap n-s leg. |
| 1021 | Turning south for the 2nd survey leg. |
| 1628 | Shifted heading reference back to geographic. |

# 7 April 1999

| 0058 | Commenced SCAMP flat-bottom calibration. This is being done in an area which seemed to be flat when we passed by northbound. |
| --- | --- |
| 0252 | Completed flat-bottom calibration. Resumed survey. |
| 0524 | Completed second Chukchi Cap survey leg. Broke track for 2-depth spiral and housekeeping. |
| 0528 | Launched XCTD #4 (Event #13) - sat. |
| 0536 | Commenced 2-depth spiral samples (also Event #13). |
| 0601 | Completed water samples. Commenced housekeeping. |
| 0639 | Completed housekeeping. Since track continuity is not important between here and the start of the 3rd leg, we’ll proceed there directly rather than regaining track. |
| 0647 | Commenced 3rd & final Chukchi Cap survey leg. This leg will be about half as long as the first two. |
| 1129 | Took brief evasive action to avoid a deep ice keel. |
| 1603 | Completed Chukchi Cap portion of the survey. Proceeding eastward to do the Northwind rise portion of this phase. We’ll do the rest of this phase at 440ft/12kts. |
| 1634 | Commenced in-line sample (Event #14). This location was selected to be over the steep portion of the eastern slope off the Chukchi Cap. We will no longer routinely slow to verify ballast but want to do it at least once here at 440 ft. We are doing it in conjunction with the in-line sample to minimize distance traveled while sampling. |
| 1644 | Completed sampling. |
| 1704 | Slowed briefly because the OOD (incorrectly) thought we were slowing for all in-line samples. |
| 1709 | Commenced in-line sample (Event #15). This site was selected to be over the deep basin between the Chukchi Cap and the Northwind Rise. |
| 1811 | Bottom is coming up rapidly. Since there are no soundings on this portion of our chart, slowed to 8 kts. |
| 1827 | Commenced in-line sample (Event #16). This is over the eastward slope of this mid-basin rise. |
| 1831 | A little more secure that the bottom is no longer coming up. Resumed 12kts. |
| 1906 | Over the next couple hours, we will make several minor adjustments to depth and heading because they were allowing the scientists & reporters to drive. Shouldn’t be too significant. |
| 2028 | Quit fooling around and resumed steady depth & speed. |

# 8 April 1999

| 0004 | Reached the vicinity of the Northwind Rise. Our survey here will consist of seven legs, oriented roughly E-W, with the track we used to get here being extended eastward to constitute the first leg. The terminus of this first leg will extend further eastward into the Canada Basin than the others. Commenced in-line sample (Event #17). This site was selected to roughly correspond to the northwestern corner of our survey. |
| --- | --- |
| 0012 | Bottom coming up rapidly. Slowed to 3 kts. |
| 0017 | Resumed 12 kts. |
| 0032 | Bottom again coming up quickly. Slowed to 3 kts. |
| 0100 | More comfortable with soundings. Increased speed to 8 kts. |
| 0112 | Resumed 12 kts. |
| 0524 | Completed 1st Northwind Rise leg. Breaking track for 3-depth hydrocast and housekeeping. Once we’re finished, the Chief Scientist desires to continue down-track another 6nm to get further into the abyssal plain. |
| 0527 | Launched XCTD #5 (Event #18) – sat. |
| 0529 | Commenced 3-depth spiral samples (also Event #18). |
| 0645 | Completed sampling. Proceeding with housekeeping. |
| 0720 | Completed housekeeping. Resuming first survey leg. |
| 0805 | Completed Leg 1. |
| 0830 | Commenced 2nd Northwind Rise leg. Because we had difficulty keeping lock on the bottom while crossing the escarpment at 12 kts on leg 1, we’ll start this leg at 8 kts until we’re up onto the plateau. |
| 0953 | We’ve crossed the escarpment. Going back to 12 kts. |
| 1436 | Completed 2nd Northwind survey leg. Going 16 kts en-route to start of 3rd leg to make up some lost time. |
| 1455 | Commenced 3rd Northwind survey leg. Resumed 12 kts. |
| 1946 | Completed 3rd Northwind survey leg. While repositioning, we’ll come shallow & slow to conduct brief housekeeping. |
| 2026 | Commenced 4th Northwind survey leg. Approaching the Northwind escarpment from the east. |
| 2138 | Took evasive action to avoid rapidly shoaling bottom. Reversing course and coming to 200ft. |
| 2203 | We’re back over deep water. We’ll approach the escarpment again at 190ft/5kts with additional watches stationed and all instruments running. |
| 2250 | Past the spot where we had the very shallow water before. We’ve seen nothing shallower than about 390fms. Here’s what we think happened the first time. The ship’s fathometer was temporarily secured because of a paper jam. Our only source of soundings was SCAMP which appears to have lost track while crossing the rapidly changing bottom and was providing phony data. We’re going back to 440ft/12kts and resuming the survey. Excitement is all over. |

# 9 April 1999

| 0253 | Completed 4th Northwind survey leg. |
| --- | --- |
| 0320 | Commenced 5th Northwind survey leg. |
| 0448 | Broke track for housekeeping and 3-depth spiral. |
| 0549 | Completed housekeeping. Returning to track to conduct spiral. |
| 0602 | Launched XCTD #6 (Event #19) – sat. |
| 0609 | Commenced 3-depth spiral samples (also Event #19). |
| 0651 | Completed samples. |
| 0704 | Resumed survey |
| 1001 | Completed 5th Northwind survey leg. We’re making yet another change to the plan. In order to provide truth tracks along the escarpment, we’ll go north from here, crossing all previous survey tracks then parallel that truth track southward past our current position to cover the last 2 e-w survey legs which we’ll complete after the truth tracks. We’ll do all of this at 440ft/12kts. |
| 1156 | Completed first truth track. Coming east to set up for second truth track. |
| 1226 | Commenced second truth track. |
| 1517 | Completed second truth track. Starting the 6th Northwind survey leg. This will be the most southerly survey leg with the last leg falling midway between this and the 5th leg. |
| 1953 | Completed 6th Northwind survey leg. |
| 2028 | Commenced 7th and final Northwind survey leg. |

# 10 April 1999

| 0126 | Completed Northwind survey. We’ll perform a 3-depth hydrocast, conduct housekeeping, then transit to the camp to complete this phase. |
| --- | --- |
| 0131 | Commenced 3-depth spiral samples (Event #20). |
| 0248 | Launched XCTD #7 (also Event #20) – sat. |
| 0255 | Completed sampling. Commenced housekeeping. |
| 0502 | Completed housekeeping. Commenced transit to the camp. En-route, we’ll draw several in-line samples (mainly just DO). |
| 1355 | Commencing camp rendezvous. Securing acoustic sensors. |
| 1514 | Maneuvering for surfacing. |
| 1631 | Commenced ascent. |
| 1635 | Surfaced at APLIS. We’ll embark the VIPs in a few hours. |

# 11 April 1999

| 0031 | Submerged. There is no science planned during this VIP underway. All along, we knew that any science we got would be a bonus. Initially, we had hoped to make a couple runs past the Northwind escarpment but the camp is further east than planned which means that just getting to the ridge and back would take longer than is comfortable (the VIPs have an early-morning plane to catch). Instead, we had planned to do a deep water flat-bottom SCAMP calibration. However, while we were just on the surface, SINS developed a problem and won’t be providing accurate positions until reset during our next surfaced period. Instead, we’ll just drive around in a box until it’s time to surface. Most data systems will be operated but no samples are planned. |
| --- | --- |
| 0109 | Started the box at 7kts/440ft. |
| 0945 | Came shallow for housekeeping. |
| 1016 | Completed housekeeping. Returned to 440 ft. |
| 1155 | Commenced camp rendezvous. |
| 1346 | Commenced ascent. |
| 1354 | Surfaced. We’ll debark the VIPs, embark Dr. Whitledge & Dr. Stockwell, and load some of the XCTD probes which were delivered here at the camp. While on the surface, we’ll also install the DO sensors on the two ICECATs. Because these are easily damaged by exposure to the cold while surfaced, we’ve put off installing these until just before the Alaska Shelf Survey. The DO sensor on ICECAT #2 is one of our standard Beckman units while the one on ICECAT #1 is a special sensor provided by Dr. Langdon. |
| 2011 | Submerged. Commenced Phase 4 – Alaska Shelf Survey. This phase will be conducted in two parts: After an initial transit to the south, we’ll spend the first three days conducting a series of 21 sawtooth legs across the Alaska continental slope. Inbound, this will be done at 440ft/16kts until we reach the 500fm isobath when we’ll come to 200ft/8kts until we reach the 150fm isobath at which point we’ll turn away. Outbound, we’ll use the same depth/speed combinations Common to all of these legs, we’ll collect water samples at the seaward endpoint, the shoreward endpoint and at both depths at the 500fm depth change. For four of the legs, we’ll launch 5 XCTDs along the leg. For three of the legs, we’ll do 8-depth spirals at the 500fm point. For two of the legs, we’ll launch an XCTD at the 500fm point. Upon completing the 21 sawtooth legs, we’ll return along the 200fm isobath at 440ft/16kts. Although not a key element of this oceanographic-driven phase, we’ll operate SCAMP (as well as all of the other data collection systems) continuously which should provide good information about the continental slope here. We have some housekeeping to do so we’ll finish it up while making our way to the start of the first sawtooth leg. |
| 2220 | Start first sawtooth leg. This will be a 5-probe leg. |
| 2223 | Launched XCTD #8. Unsat – got no data (our first failure). We’ll launch another. |
| 2229 | Launched XCTD #9 (Event #29) – sat. |
| 2236 | Resumed survey. |
| 2243 | Conducted in-line water sample (Event #29) |
| 2320 | Broke track for XCTD launch. |
| 2323 | Launched XCTD #10 (Event #30) – sat. |
| 2329 | Resumed survey. |

# 12 April 1999

| 0007 | Conducted 440 ft sample at 500 fms (Event #31). |
| --- | --- |
| 0014 | Broke track for probe launch. |
| 0017 | Launched XCTD #11 (Event #31) – sat. |
| 0028 | Resumed survey at 200 ft/8kts. |
| 0032 | Conducted 200 ft sample at 500 fms (Event #32). |
| 0108 | Broke track for probe launch (4th this leg). |
| 0111 | Launched XCTD #12 (Event #33) – sat. |
| 0116 | Resumed survey. |
| 0148 | Dr. Whitledge suggested that we use 190 ft in lieu of 200 ft to allow easy comparison to other samples taken at this “standard” depth. In order to have consistency on the next and subsequent legs, we’re coming to 190 ft now. |
| 0156 | At end of 1st sawtooth. We’ll sample and launch XCTD while we turn. Conducting 190 ft sample (Event #34). |
| 0158 | Launched XCTD #13 (also Event #34) – sat. |
| 0159 | Commenced 2nd sawtooth leg. There will be no probes this leg. |
| 0334 | Commenced 190 ft sample at 500 fms (Event #35). |
| 0338 | Came to 440ft/16kts. |
| 0342 | Commenced 440 ft sample at 500 fms (Event #36). |
| 0441 | Completed 2nd sawtooth. Started 3rd sawtooth. This will have an 8-depth spiral at the 500 fm curve. Commenced 440 ft sample (Event #37). |
| 0537 | At 500 fm curve. Broke track for housekeeping and hydrocast. We’ll do a little housekeeping first, do the hydrocast, then finish housekeeping. |
| 0647 | Launched XCTD #14 (Event #38). |
| 0700 | Commenced 8-depth samples (also Event #38). |
| 0934 | Completed sampling. Commenced housekeeping. |
| 1039 | Completed housekeeping. Resumed sawtooth a couple miles down-track from where we broke off. |
| 1219 | Completed 3rd sawtooth. Commenced 4th sawtooth. Legs 4-6 have no probe drops. Commenced 190 ft samples (Event #39). |
| 1347 | Commenced 190 ft samples at 500 fms (Event #40). |
| 1351 | Came to 440ft/16kts. |
| 1357 | Commenced 440 ft samples at 500 fms (Event #41). |
| 1522 | Approaching end of 4th sawtooth. Commenced 440 ft samples (Event #42). |
| 1524 | Completed 4th sawtooth. Commenced 5th sawtooth. |
| 1621 | Approaching 500 fms. Commenced 440 ft sample (Event #43). |
| 1644 | Came to 190ft/8kts. |
| 1648 | Commenced 190 ft samples at 500 fms (Event #44). |
| 1732 | Completed 5th sawtooth. Commenced 6th sawtooth. Commenced 190 ft samples (Event #45). |
| 1833 | Approaching 500 fms. Commenced 190 ft samples (Event #46). |
| 1837 | Came to 440ft/16kts. |
| 1840 | Commenced 440 ft samples at 500 fms (Event #47). |
| 1939 | Completed 6th sawtooth. Commenced 440 ft samples (Event #48). Commenced 7th sawtooth (single XCTD at 500 fm curve). |
| 2054 | Broke track to come to 190 ft and launch probe. Due to miscommunication, we missed the 440 ft sample at this site. |
| 2107 | Launched XCTD #15 (Event #49) – sat. |
| 2108 | Commenced 190 ft water samples at 500 fms (also Event #49) – sat. |
| 2113 | Resumed survey at 190 ft. |
| 2157 | Completed 7th sawtooth. Commenced 190 ft samples (Event #50). Commenced 8th sawtooth. Legs 8-11 have no probe launches. |
| 2236 | Commenced 190’ water sample at 500 fms (Event #51). |
| 2239 | At 500 fm curve. Came to 440ft/16kts. Missed the 440’ sample. |
| 2357 | Completed 8th sawtooth. Commenced 440 ft samples (Event #52). Commenced 9th sawtooth. |

# 13 April 1999

| 0137 | At 500 fm curve. Commenced 440 ft sample (Event #53). |
| --- | --- |
| 0140 | Came to 190ft/8kts. |
| 0149 | Commenced 190 ft sample at 500 fms (Event #54). |
| 0151 | Broke track for housekeeping. |
| 0232 | Completed housekeeping. Resumed survey. |
| 0317 | Completed 9th sawtooth. The 10th leg is another 5-probe leg so we’ll launch a probe and take a sample here before proceeding with leg 10. |
| 0319 | Launched XCTD #16 –sat; commenced water samples (both Event #55). |
| 0322 | Commenced 10th sawtooth. |
| 0340 | At 500 fm curve. We’ll sample at 190 ft then go to 440 feet for a sample and the 2nd probe on this leg. Commenced 190 ft sample (Event #56). |
| 0344 | Came to 440 ft. |
| 0350 | Commenced 440 ft samples at 500 fms (Event #57). |
| 0354 | Launched XCTD #17 (also Event #57) – sat. |
| 0400 | Resumed survey. |
| 0425 | Broke track for probe launch. |
| 0427 | Launched XCTD #18 (Event #58) – sat. |
| 0434 | Resumed survey. |
| 0507 | Broke track for probe launch. |
| 0510 | Launched XCTD #19 – no data. We’ll launch another. |
| 0516 | Launched XCTD #20 (Event #59) – sat. |
| 0522 | Resumed survey. |
| 0551 | Reaching end of 10th sawtooth. Commenced 440 ft sample (Event #60). |
| 0552 | Completed 10th sawtooth. Circling to launch the final probe on this leg. |
| 0554 | Launched XCTD #21 (also Event #60) – sat. |
| 0600 | Commenced 11th sawtooth. No probe drops on this leg. |
| 0735 | Commenced 440 ft sample at 500 fms (Event #61) |
| 0739 | Came to 190ft/8kts. |
| 0745 | Commenced 190 ft sample at 500 fms (Event #62). |
| 0853 | Commenced 190 ft end-of-leg sample (Event #63). |
| 0854 | Completed 12th sawtooth. Commenced 13th sawtooth. We will do an 8-depth spiral at the 500 fm curve on this leg. |
| 0946 | Broke track for 8-depth spiral. |
| 0949 | Launched XCTD #22 (Event #64) – sat. |
| 0950 | Commenced 8-depth samples (also Event #64). |
| 1150 | Completed sampling. |
| 1208 | Resumed track. |
| 1345 | Completed 13th sawtooth. Commenced 14th sawtooth. Legs 14 & 15 have no special requirements. |
| 1346 | Commenced 440 ft sample (Event #65). |
| 1540 | Commenced 440 ft sample at 500 fms (Event #66). |
| 1542 | Came to 190ft/8kts. |
| 1556 | Commenced 190 ft sample at 500 fms (Event #67). |
| 1608 | Completed 14th sawtooth. Commenced 15th sawtooth. Commenced 190 ft samples (Event #68). |
| 1632 | Commenced 190 ft samples at 500 fms (Event #69). |
| 1636 | Came to 440ft/16kts. |
| 1640 | Commenced 440 ft samples at 500 fms (Event #70). |
| 1840 | Completed 15th sawtooth. Commenced 16th sawtooth which will have a single probe launch at the 500 fm curve. Commenced 440 ft samples (Event #71). |
| 2045 | Commenced 440 ft sample at 500 fms (Event #72). |
| 2100 | Came to 190 feet and set up to launch probe. |
| 2104 | Commenced 190 ft sample at 500 fms (Event #73). |
| 2106 | Launched XCTD #23 (also Event #73) – sat. |
| 2112 | Resumed survey at 190ft/8kts. |
| 2133 | Completed 16th sawtooth. Commenced 17th sawtooth (nothing special). Commenced 190 ft samples (Event #74). |
| 2152 | Commenced 190 ft samples at 500 fms (Event #75). |
| 2155 | Came to 440ft/16kts. |
| 2202 | Commenced 440 ft samples at 500 fms (Event #76). |

# 14 April 1999

| 0019 | Completed 16th sawtooth. 17th sawtooth is a 5-probe leg so we’ll launch a probe here. Commenced 440 ft water samples (Event #77). |
| --- | --- |
| 0022 | Launched XCTD #24 (also Event #77) – sat. |
| 0028 | Commenced 17th sawtooth. |
| 0110 | Broke track for probe launch. |
| 0113 | Launched XCTD #25 (Event #78) – sat. |
| 0119 | Resumed track. |
| 0208 | Broke track for probe launch. |
| 0210 | Signal ejector failed leaving the probe jammed in the tube. We’ll continue to circle while we troubleshoot. |
| 0246 | Ejected probe (#26) from the signal ejector to clear it. We’ll go off and conduct housekeeping while we try to resolve the problem. |
| 0336 | Completed housekeeping. We’ll return to where we want to do the probe launch and wait to see if we can get it fixed. Currently about 10 hours ahead of schedule so we can spare the time. |
| 0509 | Believe we have the signal ejector repaired. Establishing conditions to launch probe. |
| 0510 | Launched XCTD #27 (Event #79) – sat. We’re back in business. |
| 0516 | Resumed track. |
| 0532 | Commenced 440 ft sample at 500 fms (Event #80). |
| 0533 | Came to 190ft/8kts. |
| 0538 | Commenced 190 ft water sample at 500 fms (Event #81). |
| 0545 | Broke track to launch probe. |
| 0547 | Launched XCTD #28 (Event #82) – sat. |
| 0550 | Resumed track. |
| 0614 | Completed 17th sawtooth. Broke track to launch probe. |
| 0615 | Commenced 190 ft sample at end of 17th sawtooth (Event #83). |
| 0616 | Launched XCTD #29 (also Event #83) – sat. |
| 0628 | Commenced 18th sawtooth (no special events). Shifted heading to transverse. |
| 0753 | Commenced 190 ft sample at 500 fms (Event #84). |
| 0757 | Came to 440ft/16kts. |
| 0803 | Commenced 440 ft sample at 500 fms (Event #85). |
| 0923 | Completed 18th sawtooth. Commenced 440 ft sample (Event #86). Commenced 19th sawtooth which will have an 8-depth spiral at 500 fms. |
| 1026 | Came to 190ft/8kts in preparation for 8-depth spiral. |
| 1038 | Broke track for spiral. |
| 1042 | Launched XCTD #30 (Event #87) – sat. |
| 1043 | Commenced 8-depth spiral sampling (also event #87). |
| 1235 | Completed 8–depth samples. Returning to 190ft/8kts. |
| 1249 | Resumed track. |
| 1506 | Completed 19th sawtooth. Commenced 20th sawtooth (nothing special). Commenced 190 ft sample (Event #88). |
| 1742 | Commenced 190 ft sample at 500 fms (Event #89). |
| 1746 | Came to 440ft/16kts. |
| 1749 | Commenced 440 ft sample at 500 fms (Event #90). |
| 1920 | Completed 20th sawtooth. 21st sawtooth is a 5-probe leg so we’ll set up to launch a probe here. |
| 1923 | Launched XCTD #31 (Event #91) – sat. |
| 1930 | Commenced 21st (and final) sawtooth. This will be a 5-probe leg. |
| 1934 | Commenced 440 ft sample (also Event #91). |
| 2010 | Broke track for probe launch. |
| 2013 | Launched XCTD #32 (Event #92) – sat. |
| 2019 | Resumed track. |
| 2059 | Broke track for probe launch. |
| 2102 | Launched XCTD #33 (Event #93) – sat. |
| 2115 | Resumed track. |
| 2121 | Commenced 440 ft sample at 500 fms (Event #94). |
| 2127 | Came to 190ft/8kts. |
| 2135 | Commenced 190 ft sample at 500 fms (Event #95). |
| 2136 | Broke track for probe launch. |
| 2143 | Launched XCTD #34 (also Event #95) – sat. Some delay in launching due to another minor problem with the signal ejector which was quickly resolved. |
| 2149 | Resumed track. |
| 2228 | Completed 21st sawtooth. Circling to launch final probe. |
| 2229 | Commenced 190 ft water samples (Event #96). |
| 2230 | Launched XCTD #35 (also Event #96) – sat. |
| 2237 | Completed sawtooth portion of Phase 4. We’ll now follow the 200 fm curve back westward. Rather than using segments to approximate the 200 fm curve, we’ll maneuver to attempt to stay between about 200-250 fms. We’re far enough ahead that we’ve slowed from the originally planned 16 kts down to 12 kts. If we’d used 16, we would have arrived at the ice camp too early in the day to surface & had to loiter anyway. As a preview, this sounds easier than it was to execute. The 200 fm isobath along this coast is very irregular and soundings sometimes changed by 100 fms or more in a matter of seconds. It involved far more maneuvering than we anticipated and it was fortunate that we elected to use a slower speed. We’ll take water samples approximately mid-way between the points at which we cross our sawtooth track, near the shoreward turn points. Because all of the probe budget for this phase was allocated to the sawtooth, we won’t launch any more probes this phase. |

# 15 April 1999

| 0138 | Commenced in-line sample (Event #97). |
| --- | --- |
| 0324 | Shifted heading reference back to geographic. |
| 0446 | Broke track for a 2-depth spiral. |
| 0447 | Commenced 2-depth spiral samples (Event #98). Water is too shallow to do a 750 ft sample. |
| 0552 | Diverting from our 200 fm track to go into deeper water to avoid some bottom moorings which Dr. Weingartner alerted us to (thanks Tom). |
| 1037 | Commenced in-line sample (Event #99). Completed the detour around the bottom moorings and are back following the 200 fm curve. |
| 1415 | Commenced in-line sample (Event #100). |
| 1750 | Commenced in-line sample (Event #101). |
| 2009 | Commenced in-line sample (Event #102). |
| 2234 | Commenced in-line sample (Event #103). |

# 16 April 1999

| 0100 | Commenced in-line sample (Event #104). |
| --- | --- |
| 0313 | Commenced in-line sample (Event #105). |
| 0630 | Broke track for 2-depth spiral & housekeeping. |
| 0631 | Commenced 2-depth spiral samples (Event #106). |
| 0659 | Completed samples. Commenced housekeeping. |
| 0731 | Completed housekeeping. We’ve completed the 200 fm survey. Proceeding to ice camp. |
| 1100 | Commencing camp rendezvous. Secured SCAMP to facilitate communications. |
| 1417 | On final approach for surfacing. |
| 1436 | Commenced ascent. |
| 1440 | Surfaced at APLIS for the final time. Dr. Edwards & Dr. Whitledge depart and Dr. Coakley embarks as Acting Chief Scientist. While on the surface, shift heading reference to transverse. |
| 2032 | Submerged. Commence Phase 5 – Cross-Basing Transect (northbound). We’ll go from the camp to a point off Barrow then do the transect as far as the Lomonosov Ridge. This track will parallel the track done on SCICEX-98, offset about 5nm to the right. Something new this year is that we will vary the probe spacing based upon the degree of variability we’ve seen in previous years. Dr. Mikhalevsky has designated areas for using either 16, 20, or 24 nm spacing (I’ll identify as we go along). We’ll do in-line samples at about every other probe site and 8-depth spirals at 7 locations along the route. First off, we’ll take care of some housekeeping while running down to the start point. |

# 17 April 1999

| 0239 | Reached start point for the transect. This will be our first probe drop and in-line sample. Once we leave here, we’ll initially be crossing the Beaufort Sea. The first 7 probes (this included) will be at 24nm intervals. |
| --- | --- |
| 0240 | Commenced in-line samples (Event #107). |
| 0241 | Launched XCTD #36 (also Event #107) – sat. |
| 0253 | Commenced transect. |
| 0425 | Broke track for probe launch. |
| 0427 | Launched XCTD #37 (Event #108) – sat. |
| 0438 | Resumed transect. |
| 0609 | Commenced in-line water samples (Event #109) |
| 0610 | Broke track for probe launch. |
| 0613 | Launched XCTD #38 (also Event #109) – sat. |
| 0623 | Resumed transect. |
| 0755 | Broke track for probe launch. |
| 0758 | Launched XCTD #39 (Event #110) – sat. |
| 0806 | Resumed transect. |
| 0937 | Broke track for probe launch. |
| 0940 | Commenced in-line samples and launched XCTD #40 (Event #111) – sat. |
| 0947 | Resumed transect while coming shallow for brief housekeeping. |
| 1010 | Resumed 750 ft transect. |
| 1146 | Broke track for probe launch. |
| 1149 | Launched XCTD #41 – no data. We’ll launch another. |
| 1156 | Launched XCTD #42 (Event #112) – sat. |
| 1212 | Resumed transect. |
| 1338 | Broke track for 8-depth spiral. |
| 1341 | Launched XCTD #43 (Event #113) – sat. |
| 1350 | Commenced 8-depth spiral (also Event #113). The first three spirals on this transect will take place as we approach, atop, and just after leaving the Northwind Rise. In general, we’ll start these spirals at 750 ft, spiral up to 190 ft, then return to 750 ft and resume track where we left off. We’ve standardized the depths for the samples to be at keel depths of: 190 ft / 260 ft / 330 ft / 380 ft / 440 ft / 540 ft / 640 ft / 750 ft |
| 1555 | Completed sampling. |
| 1606 | Resumed transect. We’ll now go to a 20nm probe launch interval until we’re well past the Northwind Rise. |
| 1723 | Broke track for probe launch. |
| 1732 | Launched XCTD #44 (Event #114) – sat. |
| 1745 | Resumed transect. |
| 1850 | Broke track for probe launch. Commenced in-line water samples (Event #115). |
| 1852 | Launched XCTD #45 (also Event #115) – sat. |
| 1903 | Resumed transect. |
| 2015 | Broke track for probe launch. |
| 2018 | Launched XCTD #46 (Event #116) – sat. |
| 2028 | Resumed transect. |
| 2144 | Broke track for 8-depth spiral. |
| 2148 | Launched XCTD #47 (Event #117) – sat. |
| 2150 | Commenced 8-depth spiral (also Event #117). This is the one atop the Northwind Rise. |
| 2354 | Completed sampling. Proceeding with housekeeping. |

# 18 April 1999

| 0045 | Resumed transect. |
| --- | --- |
| 0200 | Broke track for probe launch. |
| 0203 | Launched XCTD #48 (Event #118) – sat. |
| 0212 | Resumed transect. |
| 0241 | Slowed while crossing a shallow portion of the Northwind Rise. |
| 0418 | Broke track for probe launch. |
| 0420 | Launched XCTD #49 (Event #119) – sat. |
| 0426 | Commenced in-line samples (also Event #119). |
| 0428 | Resumed transect. |
| 0439 | Returned to 16 kt transit speed. |
| 0513 | Slowed again to 8 kts due to shallow water. |
| 0631 | Broke track for 8-depth hydrocast & housekeeping. This is the one just north of the Northwind Rise. |
| 0634 | Launched XCTD #50 (Event #120) – sat. |
| 0641 | Commenced 8-depth samples (also Event #120). |
| 0857 | Completed sampling. |
| 0916 | Resumed transect, at 16 kts. |
| 1040 | Broke track for probe launch. |
| 1043 | Launched XCTD #51 (Event #121) – sat. |
| 1054 | Resumed transect. |
| 1210 | Broke track for probe launch. |
| 1215 | Launched XCTD #52 (Event #122) – sat. |
| 1216 | Commenced in-line samples (also Event #122). |
| 1225 | Resumed transect. |
| 1337 | Broke track for probe launch. |
| 1341 | Launched XCTD #53 (Event #123) – sat. |
| 1354 | Resumed transect. |
| 1505 | Broke track for probe launch. |
| 1509 | Launched XCTD #54 (Event #124) – sat. |
| 1511 | Commenced in-line samples (also Event #124). |
| 1520 | Resumed transect. |
| 1536 | Slowed briefly due to shallowing waters. |
| 1541 | Resumed 16 kt transit. |
| 1546 | Came shallow for brief housekeeping. |
| 1607 | Back at 750ft/16kts. |
| 1645 | Broke track for probe launch. |
| 1648 | Launched XCTD #55 (Event #125) – sat. |
| 1657 | Resumed transect. |
| 1810 | Commenced in-line samples (Event #126) |
| 1812 | Broke track for probe launch. |
| 1815 | Launched XCTD #56 (also Event #126) – sat. |
| 1825 | Resumed transect. |
| 1940 | Broke track for probe launch. |
| 1943 | Launched XCTD #57 (Event #127) – sat. |
| 1952 | Resumed transect. |
| 2103 | Commenced in-line samples (Event #128) |
| 2109 | Broke track for probe launch. |
| 2111 | Launched XCTD #58 (also Event #128) – sat. |
| 2126 | Resumed transect. Per plan, we’re reverting back to the 24nm spacing at this point. |
| 2249 | Broke track for probe launch. |
| 2253 | Launched XCTD #59 (Event #129) – sat. |
| 2304 | Resumed transect. |

# 19 April 1999

| 0029 | Commenced in-line samples (Event #130). |
| --- | --- |
| 0030 | Broke track for probe launch. |
| 0034 | Launched XCTD #60 (also Event #130) – sat. |
| 0037 | Probe launch complete. Coming shallow for daily housekeeping. |
| 0135 | Housekeeping complete. Resumed transect. |
| 0313 | Broke track for probe launch. |
| 0316 | Launched XCTD #61 (Event #131) – sat. |
| 0327 | Resumed transect. |
| 0457 | Broke track for probe launch. |
| 0458 | Commenced in-line samples (Event #132). |
| 0501 | Launched XCTD #62 (also Event #132) – sat. |
| 0509 | Resumed transect. |
| 0641 | Broke track for probe launch. |
| 0644 | Launched XCTD #63 (Event #133) – sat. |
| 0654 | Resumed transect. |
| 0826 | Broke track for probe launch. |
| 0828 | Commenced in-line samples (Event #134). |
| 0829 | Launched XCTD #64 (also Event #134) – sat. |
| 0838 | Completed probe. Came shallow for brief housekeeping. |
| 0905 | Resumed transect. |
| 1036 | Broke track for probe launch. |
| 1039 | Launched XCTD #65 (Event #135) – sat. |
| 1050 | Resumed transect. We are shifting to a 20nm probe spacing while we cross the Alpha-Mendeleyev Ridge. |
| 1205 | Broke track for 8-depth hydrocast. This starts the second set of 3 hydrocasts during this phase. These will be launched atop the Alpha-Mendeleyev Ridge and in the deep basins on either side. This first will be on the North American side of the ridge. |
| 1206 | Commenced 8-depth spiral (Event #136). |
| 1209 | Launched XCTD #66 (also Event #136). |
| 1408 | Completed hydrocast. Conducting brief housekeeping before going back deep. |
| 1452 | Resumed transect. |
| 1611 | Broke track for probe launch. |
| 1615 | Launched XCTD #67 (Event #137) – sat. |
| 1625 | Resumed transect. |
| 1736 | Broke track for probe launch. |
| 1738 | Launched XCTD #68 – turned over but provided no data. We’ll launch another. This is only our 5th failure in 68 launches so we’re running a little better than the 10% failure rate budgeted. |
| 1744 | Launched XCTD #69 (Event #138) – sat. |
| 1748 | Commenced in-line samples (also Event #138). |
| 1758 | Resumed transect. |
| 1913 | Broke track for probe launch. |
| 1916 | Launched XCTD #70 (Event #139) – sat. |
| 1928 | Resumed transect. |
| 2040 | Broke track for probe launch. Commenced in-line samples (Event #140). |
| 2042 | Launched XCTD #71 (also Event #140) – sat. |
| 2054 | Resumed transect. |
| 2205 | Broke track for probe launch. |
| 2208 | Launched XCTD #72 (also Event #141) – sat. |
| 2220 | Resumed transect. |
| 2330 | Time for a probe launch. Even though we have a spiral & housekeeping scheduled at the next launch, we have to blow the sanitary tank. So we’ll do something different – we’ll break track now, come shallow to blow, and launch the probe from 190 ft while we’re blowing. Should save a little time. Also, we’ll skip the in-line sample which normally would be done at this station since we have a spiral at the next. |
| 2340 | Launched XCTD #73 (Event #142) – sat. |
| 2358 | Resumed transect. |

# 20 April 1999

| 0117 | Broke track for 8-depth spiral. This one is over the Alpha-Mendeleyev Ridge. |
| --- | --- |
| 0120 | Launched XCTD #74 (Event #143) – sat. |
| 0123 | Commenced 8-depth spiral (also Event #143). |
| 0315 | Completed spiral. We’ll do some quick housekeeping before going deep. |
| 0350 | Resumed transect. |
| 0505 | Broke track for probe launch. |
| 0508 | Launched XCTD #75 (Event #144) - sat. |
| 0517 | Resumed transect. |
| 0624 | Commenced in-line samples (Event #145). |
| 0633 | Broke track for probe launch. |
| 0636 | Launched XCTD #76 (also Event #145) - sat. |
| 0649 | Resumed transect. |
| 0801 | Broke track for probe launch. |
| 0805 | Launched XCTD #77 (Event #146) - sat. |
| 0815 | Resumed transect. |
| 0933 | Commenced in-line samples (Event #147). |
| 0934 | Broke track for probe launch. |
| 0937 | Launched XCTD #78 (also Event #147) - sat. |
| 0949 | Resumed transect. |
| 1105 | Broke track for probe launch. |
| 1108 | Launched XCTD #79 (also Event #148) - sat. |
| 1115 | Came shallow for housekeeping. |
| 1140 | Resumed transect. |
| 1257 | Broke track for 8-depth spiral. This is the one in the Fletcher Basin just after crossing the Alpha-Mendeleyev Ridge. |
| 1300 | Commenced 8-depth samples (Event #149). |
| 1301 | Launched XCTD #80 – no trace. We’ll launch another. |
| 1307 | Launched XCTD #81 (also Event #149) – sat. |
| 1459 | Completed sampling. |
| 1513 | Resumed transect. |
| 1606 | Broke track for probe launch. |
| 1609 | Launched XCTD #82 (Event #150) - sat. Going to 16nm spacing on probes. |
| 1620 | Resumed transect. |
| 1631 | Commenced a flat-bottom calibration. On our way across the basin (during this phase & the continuation Phase 7), we’ll do 3 of these in deep basins. The first, here, is in the Fletcher Basin. The second will be in the Nansen Basin, and the third in the Amundsen Basin. |
| 1738 | Completed flat-bottom calibration. Resumed transect. |
| 1820 | Broke track for probe launch. Commenced in-line samples (Event #151). |
| 1824 | Launched XCTD #83 (also Event #151) – sat. |
| 1833 | Completed Event #151. Going shallow quickly for housekeeping. |
| 1848 | Resumed transect. |
| 1938 | Broke track for probe launch. |
| 1942 | Launched XCTD #84 (Event #152). The trace is stretched vertically, indicating a retarded descent, but may be usable. We’ll not launch a backup for this one. |
| 1952 | Resumed transect. |
| 2045 | Commenced in-line samples (Event #153). |
| 2050 | Broke track for probe launch. |
| 2053 | Launched XCTD #85 (also Event #153). |
| 2105 | Resumed transect. |
| 2204 | Broke track for probe launch. |
| 2207 | Launched XCTD #86 (Event #154). Like probe #84, this one is stretched vertically. We’ll not launch another. |
| 2220 | Resumed transect. |
| 2330 | We’ve reached the endpoint for this phase and are scheduled to do a final 8-depth spiral. However, the boat needs to do its housekeeping first. |

# 21 April 1999

| 0126 | Completed housekeeping. Proceeding to the endpoint of Phase 5 to do the spiral. All discharges during housekeeping were at least 3000 yards from the spiral site. Since we’re already shallow, we’ll launch the probe from 190 ft and do the spiral from shallow to deep. |
| --- | --- |
| 0144 | Launched XCTD #87 (Event #155) – sat. |
| 0147 | Commenced 8-depth spiral (also Event #155). |
| 0426 | Completed spiral. This completes Phase 5. |
| 0436 | Commenced Phase 6 – Lomonosov Ridge Survey. As originally planned, we would travel south along the ridge to about 84-20N then start a series of three survey boxes, working our way from the Southern Survey Box (between about 83N and 84-20N), to the Center Survey Box (between about 86N and 87-30N), and finally the Northern Survey Box (between about 87-50N and 89N). Sampling would consist of eight 8-depth spirals (one pair on opposite ends of a Southern Box leg; a set of 3 along a Center Box leg; and a pair and a single in the Northern Box). We would also do 3-depth spirals during daily housekeeping and, unless superceded by spirals, in-line samples at the 4 corners of each box. An additional frontal survey (for Dr. Boyd) scheduled for the Northern Box will be discussed later. We’ve already made a couple changes to the plan. First, we’re extending our initial southward transit so as to start the Southern Box at its southwest corner and finish at its northeast corner (original plan had us start in the northwest and end in the southeast). This adds nothing to the time and is just an improvement over the original. The actual southbound track to the Southern Box was only 2 segments. Chief Scientist has added more segments to more closely follow the ridge which has used about an hour of his contingency time. Once reaching the southwest corner of the Southern Box, we’ll continue to follow the ridge southward for another 60nm then reverse our course and return to the box. This was intended to look for iceberg scars along the crest of the ridge and used up an additional 8 hours of Chief Scientist’s contingency time. While relocating from the northeast corner of the Southern Box to the southwest corner of the Center Box, we’ll divert slightly to pass over a potential drilling site (LORI 4). The time associated with this change is negligible. We will do the entire phase at 750ft/16kts. Except for relocation legs within and between the survey boxes, we will maintain track continuity throughout. |
| 0831 | Broke track for brief housekeeping. |
| 0859 | Resumed survey. |
| 1013 | Broke track for 8-depth spiral. This is located over the crest of the ridge in the vicinity of the Center Survey Box (during planning, this had been designated as spiral 16). When we return to do the center survey, we will conduct additional 8-depth spirals at ends of a survey leg which passes through or near this point. |
| 1015 | Launched XCTD #88 (Event #156). |
| 1022 | Commenced 8-depth samples (also Event #156). |
| 1250 | Completed sampling. |
| 1258 | Resumed survey. |
| 2111 | Broke track for brief housekeeping. |
| 2140 | Resumed survey. |

# 22 April 1999

| 0353 | Broke track for daily housekeeping. Because we are very near a point at which we’ll do an 8-depth spiral late in the Southern Survey Box, we’ll not take any samples here. |
| --- | --- |
| 0638 | Resumed survey. |
| 1012 | Broke track to come shallow for quick housekeeping. |
| 1041 | Resumed survey. |
| 1132 | We’ve reached the southern end of this transit. We’ll offset to the east the proceed to the Southern Survey Box. We’ll do an in-line sample here (Event #157). |
| 1740 | Commenced the Southern Survey Box. We’ll take an in-line sample here. The Southern Survey Box is an 11-leg boustrophedon with legs running roughly 130/310. The survey legs are offset from the crest of the ridge in order to obtain better data on the splinter ridge paralleling the Lomonosov on the North American side. |
| 1742 | Commenced in-line samples (Event #158). |
| 1932 | Broke track to come shallow for quick housekeeping. |
| 2000 | Resumed survey. |

# 23 April 1999

| 0118 | Coming to the end of the first survey leg. Commenced 3-depth spiral (Event #159). |
| --- | --- |
| 0119 | Broke track for 3-depth spiral and housekeeping. |
| 0122 | Launched XCTD #89 (also Event #159) – sat. |
| 0200 | Completed spiral. Proceeding with housekeeping. Since track continuity is not important on this connector leg, we’ll resume the survey at the start of the second survey leg. This will be true for all connector legs during this survey. |
| 0421 | Commenced Leg 2. |
| 1129 | Completed 2nd leg of the Southern Survey Box. Coming shallow for a quick housekeeping while we reposition. |
| 1210 | Commenced Leg 3. |
| 1738 | Slowed to 10 kts due to unexpectedly shallow soundings. |
| 1845 | Resumed 16 kts. |
| 1945 | Decided to do quick in-line samples at the end of each leg when we’re not doing spirals. Commenced in-line samples at endpoint of Leg 3 (Event #160). |
| 1946 | Completed Leg 3. We’ll come shallow for housekeeping during the repositioning (didn’t leave 750 ft until in-line sample was completed). |
| 2015 | Completed housekeeping. |
| 2025 | Commenced Leg 4. |

# 24 April 1999

| 0315 | Completed Leg 4. Broke track for 3-depth spiral and daily housekeeping. |
| --- | --- |
| 0318 | Launched XCTD #90 (sat) and commenced 3-depth spiral sampling (Event #161). |
| 0406 | Completed sampling. Proceeding with housekeeping. |
| 0547 | Housekeeping complete. |
| 0618 | Commenced Leg 5. |
| 1250 | Nearing the end of Leg 5. Commenced in-line samples (Event #162). |
| 1252 | Completed Leg 5. Coming shallow for brief housekeeping. |
| 1314 | Housekeeping complete. |
| 1336 | Commenced Leg 6. |
| 1949 | Completed Leg 6. Commenced in-line samples (Event #163). |
| 1951 | In-line samples complete. Coming shallow for quick housekeeping while repositioning. |
| 2015 | Housekeeping complete. |
| 2029 | Commenced Leg 7. |

# 25 April 1999

| 0227 | Completed Leg 7. Stopping for daily housekeeping and a 3-depth spiral. Commenced 3-depth samples (Event #164). |
| --- | --- |
| 0230 | Launched XCTD #91 (also Event #164) – sat. |
| 0321 | Completed spiral. Proceeding with housekeeping. |
| 0406 | Completed housekeeping. |
| 0427 | Commenced Leg 8. |
| 1020 | Approaching end of Leg 8. Commenced in-line samples (Event #165). |
| 1023 | Completed sampling. Coming shallow for brief housekeeping while repositioning. |
| 1046 | Completed housekeeping. |
| 1100 | Commenced Leg 9. |
| 1654 | Approaching end of Leg 9. Commenced in-line samples (Event #166). |
| 1656 | Completed sampling. Coming shallow for brief housekeeping while repositioning. |
| 1721 | Completed housekeeping. |
| 1740 | Commenced Leg 10. |
| 2315 | Completed Leg 10. Skipping the in-line sample here since we’ll be doing an 8-depth spiral at the start of the next leg. Coming shallow for brief housekeeping while repositioning. |
| 2334 | Completed housekeeping. |
| 2349 | Reached the start point of Leg 11. We’re scheduled to do 8-depth spirals at both ends of this leg. For now our plan is to do the 8-depth spiral here, then do our full daily housekeeping before starting the leg. |
| 2352 | Launched XCTD #92 (Event #167) – sat. |
| 2356 | Commenced 8-depth spiral samples (also Event #167). |

# 26 April 1999

| 0225 | Completed 8-depth spiral. Proceeding with housekeeping. |
| --- | --- |
| 0405 | Unable to complete the communications part of housekeeping. We’ll proceed with Leg 11 then try again afterward. |
| 0427 | Commenced Leg 11. |
| 0952 | Completed Leg 11. This completes the Southern Survey Box. We’ll proceed with housekeeping then return to the endpoint of Leg 11 to do the 8-depth spiral and proceed on. |
| 1345 | Completed housekeeping. Proceeding to Leg 11 endpoint. |
| 1415 | Reached the point. Commenced an 8-depth spiral (Event #168) going from shallow to deep. |
| 1423 | Launched XCTD #93 (also Event #168) – sat. |
| 1643 | Completed spiral. We’ll now proceed to the Center Survey Box. Since our southbound track along the ridge already covered the LORI-4 site, we’ve revised this transit to go from the northeast corner of the Southern Survey Box to the southeast corner of the Center Survey Box. In addition, since this runs us along the small splinter ridge paralleling the Lomonosov, the Chief scientist has used some of his contingency time to set up a series of crossings of the splinter ridge. |
| 1837 | We need to surface in order to communicate. To facilitate finding a surfaceable feature, the Chief Scientist has agreed to conducting this sawtooth survey at 440 ft instead of 750 ft. This makes the sidescan display better and allows us to see the ice on SRVS. |
| 2100 | Commenced in-line samples (Event #169). While making this transit to the Center Survey Box, we’ll take a small set of in-line samples about every 2 hours. |
| 2127 | Broke track to come shallow for brief housekeeping. |
| 2155 | Resumed survey |
| 2300 | Commenced in-line samples (Event #170). |

# 27 April 1999

| 0100 | Commenced in-line samples (Event #171). |
| --- | --- |
| 0115 | Found a possible surfaceable feature. Broke track to take another look. |
| 0141 | Making preparations to surface. Secured ADCP to avoid interference with the sidescan sonar while we map. |
| 0322 | On final approach. |
| 0341 | Commenced ascent. |
| 0349 | Surfaced through about 8 inches of new ice. |
| 0625 | Submerged. |
| 0706 | Resumed survey. |
| 0900 | Commenced in-line samples (Event #173). |
| 0954 | Broke track to come shallow for a brief housekeeping. |
| 1015 | Resumed survey. |
| 1100 | Commenced in-line samples (Event #173). |
| 1300 | Commenced in-line samples (Event #174). |
| 1449 | Commenced in-line samples (Event #175). |
| 1933 | At start point for the Center Survey Box. We’ll take an in-line sample here then come shallow for a brief housekeeping. Commenced in-line samples (Event #176). |
| 1936 | Broke track to come shallow for housekeeping. |
| 2002 | Commenced Center Survey Box Leg 1. The Center Survey Box is an 11-leg boustrophedon with legs oriented roughly 135/315. |

# 28 April 1999

| 0118 | Completed Leg 1. We had extended the leg at Chief Scientist’s request in order to get out onto the abyssal plain. We’ll stop here for our daily housekeeping and a 3-depth hydrocast. |
| --- | --- |
| 0120 | Launched XCTD #94 (Event #177) – sat. |
| 0123 | Commenced 3-depth samples (also Event #177). |
| 0212 | Completed sampling. Proceeding with housekeeping. Again, we’re not maintaining track continuity on the repositioning legs. |
| 0320 | Completed housekeeping. |
| 0345 | Commenced Leg 2. |
| 0855 | Reached the end of Leg 2. Commenced in-line samples (Event #178). |
| 0857 | Broke track to come shallow for a brief housekeeping. |
| 0919 | Completed housekeeping. |
| 0939 | Commenced Leg 3. |
| 1407 | Completed Leg 3. Will skip the in-line here since we’ll be doing an 8-depth spirals at the start of Leg 4. |
| 1426 | Reached the start point of Leg 4. Broke off for an 8-depth spiral. This is the first of a pair (both ends of Leg 4) which will straddle the spiral we did on 21 April (Event #156). |
| 1429 | Commenced 8-depth spiral samples & launched XCTD #95 (Event #179). |
| 1608 | Completed 8-depth spiral. We’ll do some quick housekeeping before we start Leg 4. |
| 1636 | Commenced Leg 4. |
| 2105 | Completed Leg 4. Breaking off to conduct the second in this pair of 8-depth spirals. |
| 2108 | Launched XCTD #96 (Event #180) – sat. |
| 2116 | Commenced 8-depth spiral samples. |
| 2300 | Completed 8-depth spiral. Again, we’ll do some quick housekeeping before resuming. |
| 2320 | Completed housekeeping. |
| 2339 | Commenced Leg 5. |

# 29 April 1999

| 0429 | Approaching the end of Leg 5. We’ll be stopping for daily housekeeping. Since we did an 8-depth spiral nearby yesterday (Event # 179), we’ll just do an in-line sample here. Commenced in-line samples (Event #181). |
| --- | --- |
| 0433 | Completed sampling. Coming shallow for daily housekeeping |
| 0540 | Completed housekeeping. |
| 0600 | Commenced Leg 6 |
| 1100 | Completed Leg 6. Somehow, we missed the in-line sample here and the boat is not stopping for housekeeping as usual. |
| 1120 | Commenced Leg 7. |
| 1156 | Recognized that we missed the in-line sample at the end of Leg 6. Took one here (Event #182). |
| 1227 | Couldn’t make it all the way through 2 legs without housekeeping. Broke track to come shallow briefly. |
| 1257 | Resumed survey. |
| 1601 | Completed Leg 7. |
| 1607 | Commenced in-line samples (Event #183). |
| 1633 | Commenced leg 8. |
| 2022 | Broke track to come shallow for a brief housekeeping. |
| 2105 | Resumed survey. |
| 2134 | Completed Leg 8. Commenced in-line samples (Event #184). |
| 2154 | Commenced Leg 9. |

# 30 April 1999

| 0143 | Completed Leg 9. We’ll stop here for our daily housekeeping and a 3-depth spiral. |
| --- | --- |
| 0147 | Launched XCTD #97 (Event #185) – sat. |
| 0148 | Commenced 3-depth spiral samples (also Event #185). |
| 0229 | Completed sampling. Proceeding with housekeeping. |
| 0322 | Completed housekeeping. |
| 0344 | Commenced Leg 10. |
| 0729 | Completed Leg 10 |
| 0808 | Commenced Leg 11 |
| 1200 | Completed Leg 11. This completes the Center Survey Box. We’ll come shallow for a brief housekeeping here then start the short transit to the Northern Survey Box. |
| 1230 | Completed housekeeping. |
| 1309 | Reached the start point of the Northern Survey Box. This has been modified heavily from the original plan to take less time. It starts with 6 legs parallel to and straddling the cross-basin transect then dog-legs to the right to conform with the ridge axis for a few more legs. We’ll have to break off in time to reach the North Pole about noon on the 3rd. Although additional survey could be done following the North Pole surfacing, the Acting Chief Scientist has chosen instead to apply that time to later phases. Dr. Boyd had laid out a pattern of 20 probes at points at which rows parallel to the cross-basin transect intersected the original track. That’s had to be changed but is much simpler now that the survey lines have been re-oriented to be parallel to the transect. We’ve also moved the three 8-depth hydrocasts slightly to take best advantage of this new pattern. We’ll do 2 of these at opposite ends of the first leg and the third at the end of the first dog-leg line such that it is approximately opposite the spiral we did when we first broke off the transect on 21 April (Event #155). We’ll do the first of these now. |
| 1311 | Commenced 8-depth spiral samples (Event #187). |
| 1313 | Launched XCTD #98 (also Event #187). |
| 1425 | Completed 8-depth spiral. |
| 1431 | Commenced Northern Survey Box Leg 1. This leg is slightly longer than the others so, in addition to the 8-depth spirals at both ends, we’ll do 5 probe launches in between at about 16nm intervals. |
| 1508 | Broke track for probe launch. We’ll also do small in-line samples (nuts & salts) with each of these Boyd probe launches. |
| 1509 | Commenced in-line samples (Event #188). |
| 1512 | Launched XCTD #99 (also Event #188) – sat. |
| 1523 | Resumed survey. |
| 1613 | Broke track for probe launch. |
| 1616 | Commenced in-line samples (Event #189). |
| 1618 | Launched XCTD #100 (also Event #189) – sat. We’ve now used up 100 probes (about 2/3 of our inventory. So far, only had 6 failures. Doing better than the 10% failure rate we budgeted which has allowed us do a couple extra daily launches along the Lomonosov and give dr. Boyd all 20 probes he requested. |
| 1630 | Resumed survey. |
| 1720 | Broke track for probe launch. |
| 1721 | Commenced in-line samples (Event #190). |
| 1726 | Launched XCTD #101 (also Event #190) – sat. |
| 1740 | Resumed survey. |
| 1826 | Broke track for probe launch. |
| 1829 | Launched XCTD #102 (Event #191) – sat. |
| 1830 | Commenced in-line samples (also Event #191). |
| 1840 | Resumed survey. |
| 1922 | Broke track for probe launch. Commenced in-line samples (Event #192). |
| 1925 | Launched XCTD #103 (also Event #192) – sat. |
| 1935 | Resumed survey. |
| 2030 | Completed Leg 1. We’ll stop here to do another 8-depth spiral. |
| 2033 | Launched XCTD #104 (Event #193) – sat. |
| 2035 | Commenced 8-depth spiral samples (also Event #193). |
| 2210 | Completed 8-depth spiral. |
| 2323 | Commenced Leg 2. This and the two legs immediately following will each have 4 probe launches spaced at about 16nm intervals. |

# 1 May 1999

| 0021 | Broke track for probe launch. |
| --- | --- |
| 0022 | Commenced in-line samples (Event #194). |
| 0025 | Launched XCTD #105 (also Event #194). |
| 0037 | Resumed survey. |
| 0130 | Broke track for probe launch. Commenced in-line samples (Event #195). |
| 0134 | Launched XCTD #106 (also Event #195). |
| 0143 | Resumed survey. |
| 0235 | Broke track for probe launch. Commenced in-line samples (Event #196). |
| 0238 | Launched XCTD #107 (also Event #196). |
| 0252 | Resumed survey. |
| 0338 | Broke track for probe launch. Commenced in-line samples (Event #197). |
| 0341 | Launched XCTD #108 (also Event #197). |
| 0352 | Resumed survey. |
| 0512 | Completed Leg 2. Broke for daily housekeeping. Since we did an 8-depth spiral about 12nm to the south, we’ll not bother with any samples here. |
| 0621 | Completed housekeeping. |
| 0626 | Commenced Leg 3. |
| 0748 | Broke track for probe launch. Commenced in-line samples (Event #198). |
| 0751 | Launched XCTD #109 (also Event #198). |
| 0812 | Resumed survey. |
| 0843 | Broke track for probe launch. Commenced in-line samples (Event #199). |
| 0845 | Launched XCTD #110 (also Event #199). |
| 0855 | Resumed survey. |
| 0943 | Commenced in-line samples (Event #200). |
| 0948 | Broke track for probe launch. |
| 0951 | Launched XCTD #111 (also Event #200). |
| 1001 | Resumed survey. |
| 1051 | Broke track for probe launch. |
| 1055 | Launched XCTD #112 (Event #201). |
| 1059 | Commenced in-line samples (also Event #201). |
| 1105 | Resumed survey. |
| 1156 | Completed Leg 3. Coming shallow for a brief housekeeping while repositioning. |
| 1219 | Completed housekeeping. |
| 1236 | Commenced Leg 4. |
| 1325 | Broke track for probe launch. |
| 1327 | Commenced in-line samples (Event #202). |
| 1330 | Launched XCTD #113 (also Event #202). |
| 1342 | Resumed survey. |
| 1430 | Broke track for probe launch. |
| 1432 | Commenced in-line samples (Event #203). |
| 1433 | Launched XCTD #114 (also Event #203). |
| 1445 | Resumed survey. |
| 1531 | Broke track for probe launch. |
| 1532 | Commenced in-line samples (Event #204). |
| 1534 | Launched XCTD #115 (also Event #204). |
| 1546 | Resumed survey. |
| 1631 | Broke track for probe launch. |
| 1632 | Commenced in-line samples (Event #205). |
| 1634 | Launched XCTD #116 (also Event #205). |
| 1645 | Resumed survey. |
| 1749 | Completed Leg 4. |
| 1840 | Came shallow for brief housekeeping. |
| 1927 | Completed housekeeping. Commenced Leg 5. This is the last leg for the Boyd launches – there will be only 3 on this leg. |
| 2100 | Broke track for probe launch. |
| 2101 | Commenced in-line samples (Event #206). |
| 2103 | Launched XCTD #117 (also Event #206). |
| 2114 | Resumed survey. |
| 2204 | Broke track for probe launch. |
| 2207 | Commenced in-line samples and Launched XCTD #118 (Event #207). |
| 2216 | Resumed survey. |
| 2308 | Broke track for probe launch. |
| 2312 | Launched XCTD #119 (Event #208). |
| 2313 | Commenced in-line samples (also Event #208). |
| 2322 | Resumed survey. This completes the series of 20 launches for Dr. Boyd. |

# 2 May 1999

| 0014 | Completed Leg 5. Broke track for daily housekeeping and 3-depth spiral. |
| --- | --- |
| 0018 | Commenced 3-depth samples (Event #209). Launched XCTD #121 – conductivity was good but temperature was constant at 26.6ºF. We’ll launch a second probe. |
| 0022 | Launched XCTD #122 (also Event #209) – sat. |
| 0105 | Completed 3-depth samples. Proceeding with housekeeping. |
| 0139 | Completed housekeeping. |
| 0155 | Commenced Leg 6. |
| 0447 | Completed Leg 6. Commenced Leg 7. This is the point at which we re-orient the axis of the survey by about 20º and go straight from Leg 6 to Leg 7. |
| 0723 | Completed Leg 7. Broke track to conduct the final 8-depth spiral for this phase. |
| 0726 | Commenced 8-depth samples & launched XCTD #123 (both Event #210). |
| 0909 | Completed 8-depth sampling. |
| 0933 | Back on track. |
| 0950 | Commenced Leg 8 |
| 1133 | Broke track to come shallow because of a fire. |
| 1140 | Resumed track. The fire was very minor. |
| 1330 | Completed Leg 8. Broke track to come shallow for brief housekeeping. |
| 1400 | Back on track. |
| 1419 | Commenced Leg 9. |
| 1810 | Completed Leg 9. |
| 1833 | Commenced Leg 10. |
| 2210 | Broke track to come shallow for brief housekeeping. |
| 2246 | Resumed track. |
| 2323 | Completed Leg 10. |
| 2342 | Commenced Leg 11. |

# 3 May 1999

| 0426 | Completed Leg 11. Broke track for daily housekeeping. Since this is relatively near where we did the 8-depth spiral yesterday, we’ll take no samples. |
| --- | --- |
| 0620 | Completed housekeeping. Commenced Leg 12. We want to be at the North Pole about noon. Since this leg is taking us away from the pole, we’ll terminate it in time to make this deadline. |
| 0657 | This is as far as we’ll go on Leg 12. We’ll relocate about 5nm further along the survey pattern so that our northbound transit will constitute another partial leg (which we’ll call 13). |
| 0728 | Commenced Leg 13. Since this takes us very near the pole, we’ll continue on this general heading even after we’ve exceeded the nominal bounds of the survey box. |
| 0945 | Secured data collection while we searched for a place to surface. |
| 1005 | Passed through (beneath?) the North Pole. |
| 1233 | Found a potential surfaceable feature. |
| 1346 | The feature is large but relatively thin and fairly broken up. We’re making final approach on what looks like the best spot which may be about 1½ feet thick. |
| 1359 | In position to surface. |
| 1405 | Commenced ascent. |
| 1410 | Surfaced through 18 inches of ice. This is a good enough spot so we’ll stay here. While on the surface, the water guys collected large volumes to be used as mementos so they are calling this location Event #211 even though no science samples were taken. |
| 2212 | Submerged. |
| 2323 | Ready to go again. We need to get back to where we broke off from the cross-basin transect to end this phase. En-route, we’ll make a slight dogleg to add one more sample line. This extra line (Leg 14) will fill in part of the angle created when we changed the survey axis between Legs 6&7. |

# 4 May 1999

| 0232 | Start Leg 14. |
| --- | --- |
| 0523 | Reached the point at which we interrupted the transect at the end of Phase 5 to do phase 6. This completes Phase 6. Start Phase 7 – the continuation of the cross-basin transect. We’ll complete the transect started in Phase 5 by launching an additional 22 XCTDs. Because there is a lot of variability throughout this area, we will use 16nm spacing for all of the probes. We won’t launch one here since we did that at the end of Phase 5 so the next will be 16nm down-track. As before, we’ll do in-line samples every other probe launch. In addition, we’ll do two 8-depth spirals, one in the Nansen Basin and the other in the Amundsen Basin. We’ll also do flat-bottom calibrations at both of the spiral sites. |
| 0621 | Broke track for probe launch. |
| 0622 | Commenced in-line samples (Event #212). |
| 0624 | Launched XCTD #123 (also Event #212) – sat. |
| 0633 | Resumed transect. |
| 0734 | Broke track for probe launch. |
| 0737 | Launched XCTD #124 (Event #213) – sat. |
| 0747 | Resumed transect. |
| 0809 | Broke track to come shallow for brief housekeeping. |
| 0836 | Resumed transect. |
| 0904 | Broke track for probe launch. |
| 0905 | Commenced in-line samples (Event #214). |
| 0907 | Launched XCTD #125 (also Event #214) – sat. |
| 0918 | Resumed transect. |
| 1019 | Broke track for probe launch. |
| 1022 | Launched XCTD #126 (Event #215) – sat. |
| 1033 | Resumed transect. |
| 1133 | Broke track for probe launch. |
| 1134 | Commenced in-line samples (Event #216). |
| 1136 | Launched XCTD #127 (also Event #216) – sat. |
| 1146 | Resumed transect. |
| 1247 | Broke track for probe launch. |
| 1252 | Launched XCTD #128. Trace was similar to that for #120 in that conductivity appeared good but the temperature was flat-lined at 26.6ºF. We’ll launch another. |
| 1259 | Launched XCTD #129 (Event #217) – sat. |
| 1307 | Resumed transect. |
| 1411 | Broke track for 8-depth spiral. |
| 1412 | Commenced 8-depth samples (Event #218). |
| 1415 | Launched XCTD #130 (also Event #218) – sat. |
| 1541 | Completed samples. Proceeding with daily housekeeping. |
| 1633 | Resumed transect. |
| 1708 | Commenced flat-bottom calibration. |
| 1808 | Completed flat-bottom calibration. Resumed transect. |
| 1826 | Broke track for probe launch. |
| 1830 | Launched XCTD #131 (Event #219) – sat. |
| 1840 | Resumed transect. |
| 1940 | Commenced in-line samples (Event #220). |
| 1941 | Broke track for probe launch. |
| 1945 | Launched XCTD #132 (also Event #220) – sat. |
| 1956 | Resumed transect. |
| 2055 | Broke track for probe launch. |
| 2057 | Launched XCTD #133 (Event #221) – sat. |
| 2109 | Resumed transect. |
| 2211 | Broke track for probe launch. Commenced in-line samples (Event #222). |
| 2214 | Launched XCTD #134 (also Event #222) – sat. |
| 2233 | Resumed transect. |
| 2330 | Broke track for probe launch. |
| 2336 | Launched XCTD #135. Lost continuity just before turnover – suspect it impacted a keel. We’ll launch another. |
| 2342 | Launched XCTD #136 (Event #223) – sat. |
| 2352 | Resumed transect. |

# 5 May 1999

| 0053 | Broke track for probe launch. |
| --- | --- |
| 0054 | Commenced in-line samples (Event #224). |
| 0058 | Launched XCTD #137 (also Event #224) – sat. |
| 0108 | Resumed transect. |
| 0209 | Broke track for probe launch and a brief housekeeping. |
| 0212 | Launched XCTD #138 (Event #225) – sat. |
| 0250 | Resumed transect. |
| 0343 | Broke track for probe launch. Commenced in-line samples (Event #226). |
| 0347 | Launched XCTD #139 (also Event #226) – sat. |
| 0357 | Resumed transect. |
| 0456 | Broke track for probe launch. |
| 0459 | Launched XCTD #140 (Event #227) – sat. |
| 0512 | Resumed transect. |
| 0609 | Broke track for probe launch. |
| 0611 | Launched XCTD #141 (Event #228) – sat. |
| 0622 | Commenced in-line samples (also Event #228). |
| 0627 | Resumed transect. |
| 0724 | Broke track for probe launch. |
| 0726 | Launched XCTD #142 (Event #229) – sat. |
| 0736 | Resumed transect. |
| 0834 | Broke track for probe launch. |
| 0835 | Commenced in-line samples (Event #230). |
| 0837 | Launched XCTD #143 (also Event #230) – sat. |
| 0850 | Resumed transect. |
| 0948 | Broke track for probe launch. |
| 0951 | Launched XCTD #144 (Event #231) – no trace but we don’t have enough left to shoot a backup. |
| 1000 | Resumed transect. |
| 1008 | Broke track to come shallow for a brief housekeeping. |
| 1037 | Resumed transect. |
| 1121 | Broke track for probe launch & 8-depth spiral. Commenced 8-depth samples (Event #232) |
| 1123 | Launched XCTD #145 (also Event #232) – another stretched trace but believed usable. |
| 1250 | Completed samples. Proceeding with daily housekeeping. |
| 1405 | Resumed transect. |
| 1450 | Commenced flat-bottom calibration. |
| 1553 | Completed flat-bottom calibration. |
| 1609 | Broke track for last probe launch in the Cross-Basin Transect. |
| 1614 | Launched XCTD #146 (Event #213) – turned over but provided no trace. No backup. We had really good probe success early in the cruise – only 6 failures in the first 119 probes (for a success rate of 97%). This was much better than the 90% budgeted. Based on this, we launched a couple extra during Phase 6. Then, during a stretch of 27 launches since the end of the Boyd survey (probes #120-146), we’ve had 5 failures. This temporary reduction in success rate (to 81%), cut into all of our reserves. Our overall success rate, however, is 92% - same as last year. It’s just that we got lulled by the good early successes. |
| 1617 | Completed Phase 7 – Cross-Basin Transect. We’ll now start Phase 8 – AMOR Survey. Per the original plan, Phase 8 was to consist of a brief transit from here to the AMOR then a run eastward down the ridge axis as far as the Data Release Area boundary, returning westward along the axis offset slightly to the north. We would then to a 23-leg, north-south boustrophedon survey of that part of the ridge west of the area surveyed in SCICEX-98. There was also an option for an added 5-leg survey to fill in the area between the two SCICEX-98 survey boxes. Two 8-depth spirals were scheduled on the axial legs and another pair on opposite ends of one of the main survey’s boustrophedon legs, but no other water sampling. A surfacing was scheduled late in the phase to do a final navigation tie. With only about a week left in data collection, the ship has turned over all of its contingency time to the Acting Chief Scientist with the understanding that anything which hold us up comes out of his survey time. Armed with this, the Chief Scientist has made the following changes. Implemented the optional survey between the 2 SCICEX-98 boxes. Looking ahead to Phase 9 (Yermak Plateau), designed a 1¼-day survey of the Yermak which was not in the original plan. Cut the axial legs to make up the time added above. Postponed the surfacing until Phase 9. Commenced transit to the AMOR. |
| 2007 | Broke track to come shallow for a brief housekeeping. |
| 2050 | Resumed transit. |
| 2303 | Slowed momentarily due to uncertain soundings. |
| 2315 | Resumed 16kt transit. |

# 6 May 1999

| 0113 | We’re at the start of the eastbound axial survey leg. Broke track for daily housekeeping. |
| --- | --- |
| 0220 | Completed housekeeping. |
| 0232 | Commenced eastbound axial leg. |
| 0948 | Broke track to come shallow for a brief housekeeping. |
| 1012 | Resumed survey. |
| 1312 | At end of eastbound axial. Broke track for 8-depth spiral. Commenced 8-depth samples (Event #234). |
| 1315 | Launched XCTD #147 (also Event #234) – sat. |
| 1436 | Completed samples. |
| 1450 | Back on depth, proceeding to start point of westbound axial leg. |
| 1508 | Start eastbound axial survey leg. |
| 2149 | Broke track to come shallow for brief housekeeping. |
| 2228 | Resumed survey. |
| 2338 | Broke track for second of the axial 8-depth spirals and daily housekeeping. |
| 2341 | Launched XCTD #148 (Event #235) – sat. |
| 2348 | Commenced 8-depth spiral samples (also Event #235). |

# 7 May 1999

| 0135 | Resumed transit. |
| --- | --- |
| 0450 | Slowed to 8 kts while passing a charted shallow area. |
| 0830 | Resumed 16 kt transit. |
| 0945 | Commenced the Optional Survey. This will be a 5-legs boustrophedon survey with legs oriented roughly 300/120. Because we start and end on the ridge axis, the first and fifth legs will be half-legs. |
| 1141 | Completed Leg 1. |
| 1202 | Commenced Leg 2. |
| 1530 | Completed Leg 2. Coming shallow for brief housekeeping while repositioning. |
| 1600 | Completed housekeeping. |
| 1625 | Commenced Leg 3. |
| 1952 | Completed Leg 3. |
| 2017 | Commenced Leg 4. |
| 2207 | Broke track to come shallow for brief housekeeping. |
| 2253 | Resumed survey. |

# 8 May 1999

| 0025 | Completed Leg 4. |
| --- | --- |
| 0102 | Commenced Leg 5. |
| 0252 | Completed optional survey. Broke track for daily housekeeping and 3-depth spiral. |
| 0256 | Commenced 3-depth samples & launched XCTD #149 (Event #236). |
| 0339 | Completed sampling. Proceeding with daily housekeeping. |
| 0442 | Completed housekeeping. |
| 0452 | Commenced transit along AMOR crest to reach main AMOR Survey area. |
| 1003 | Commenced main AMOR boustrophedon survey. This will be a 23-leg boustrophedon survey with legs running roughly 120/300. We’ve opened the ridge crest so that, unlike the optional survey, the first leg is full-length. |
| 1228 | Broke track to come shallow for brief housekeeping. |
| 1307 | Resumed survey. |
| 1403 | Completed Leg 1. |
| 1438 | Commenced Leg 2. |
| 1754 | Completed Leg 2. |
| 1813 | Commenced Leg 3. |
| 2133 | Completed Leg 3. Came shallow for brief housekeeping while repositioning. |
| 2233 | Commenced Leg 4. |

# 9 May 1999

| 0148 | Completed Leg 4. Broke track to conduct daily housekeeping on the connecting leg. |
| --- | --- |
| 0250 | Completed housekeeping. |
| 0321 | Commenced Leg 5. |
| 0637 | Completed Leg 5. |
| 0706 | Commenced Leg 6. |
| 1012 | Completed Leg 6. |
| 1037 | Commenced Leg 7. |
| 1151 | Broke track to come shallow for brief housekeeping. |
| 1219 | Completed housekeeping. Resumed survey. |
| 1407 | Completed Leg 7. |
| 1428 | Commenced Leg 8. |
| 1743 | Completed Leg 8. |
| 1756 | Commenced Leg 9. |
| 2022 | Broke track to come shallow for brief housekeeping. |
| 2106 | Resumed survey. |
| 2149 | Completed Leg 9. |
| 2210 | Commenced Leg 10. |
| 2306 | Bottom is coming up rapidly. Slowing to 12 kts until soundings stabilize (passing a seamount). |
| 2310 | Reversed course and came shallow in response to soundings being a few hundred fathoms less than charted. |
| 2318 | Soundings are deep once more. We’ll reverse course and approach again at a depth of 440 ft. |
| 2330 | Resuming survey at 440 ft. We’ll stay at this depth until we clear this seamount on our next pass (Leg 11). |

# 10 May 1999

| 0135 | Completed Leg 10. We’re planning to do a final pair of 8-depth spirals at opposite ends of Leg 11. We’ll do one here on this connecting leg and the other at the completion of Leg 11. In order to get started on this one, we’ll make the turn onto the connecting leg and change depth down to 750 feet. Once there, we’ll launch the probe and do a deep-to-shallow spiral like usual. |
| --- | --- |
| 0145 | Commenced 8-depth samples (Event # 237). |
| 0147 | Launched XCTD #150 (also Event #237) – sat. |
| 0301 | Completed sampling. Proceeding with daily housekeeping. |
| 0347 | Completed housekeeping. |
| 0358 | Commenced Leg 11 (still at 440 ft). |
| 0627 | We’re past the seamount which caused us concern on the last pass and are returning to 750 ft. |
| 0707 | Completed Leg 11. Broke track for the final 8-depth spiral. |
| 0710 | Commenced 8-depth samples and launched XCTD #151 (Event #238). |
| 0827 | Completed sampling. We only have 2 probes left. Although none were originally budgeted for Phase 9, the additions to that phase made by the Acting Chief Scientist will increase its duration from 16 hrs to about 2 days. In order to have some oceanography during Phase 9, we’ll move the last 2 daily 3-depth probes & samples from Phase 8 to Phase 9. Consequently, we’ll do no more probes or samples this phase. |
| 0838 | Resumed survey. |
| 0856 | Commenced Leg 12. |
| 1155 | Completed Leg 12. |
| 1217 | Commenced Leg 13. |
| 1517 | Completed Leg 13. |
| 1543 | Commenced Leg 14. |
| 1816 | Broke track to come shallow for brief housekeeping. |
| 1844 | Resumed survey. |
| 1915 | Completed Leg 14. |
| 1937 | Commenced Leg 15. |
| 2237 | Completed Leg 15. |
| 2301 | Commenced Leg 16. |

# 11 May 1999

| 0157 | Completed Leg 16. Broke track to conduct daily housekeeping on the connecting leg. |
| --- | --- |
| 0300 | Completed housekeeping. |
| 0320 | Commenced Leg 17. |
| 0618 | Completed Leg 17. |
| 0643 | Commenced Leg 18. |
| 0938 | Completed Leg 18. Coming shallow on the connecting leg for brief housekeeping. |
| 1004 | Completed housekeeping. |
| 1030 | Commenced Leg 19. |
| 1318 | Completed Leg 19. |
| 1345 | Commenced Leg 20. |
| 1645 | Completed Leg 20. |
| 1706 | Commenced Leg 21. |
| 1904 | Broke track to come shallow for brief housekeeping. |
| 1936 | Resumed survey. |
| 2036 | Completed Leg 21. |
| 2100 | Commenced Leg 22. |
| 2352 | Completed Leg 22. Broke track to conduct daily housekeeping on the connecting leg. |

# 12 May 1999

| 0108 | Completed housekeeping. |
| --- | --- |
| 0133 | Commenced Leg 23. |
| 0357 | Completed Leg 23. This completes the AMOR survey and completes Phase 8. So ... Commenced Phase 9. Phase 9 was originally planned to be a transit from where we are now to our egress point at 80N, doing a slight dog-leg to run down the main axis of the Yermak Plateau. By scavenging time from the Lomonosov Ridge and AMOR survey and combining all remaining contingency time, the Chief Scientist has freed up about 1¼ days to do a boustrophedon survey at the eastern tip of the plateau. Water sampling will be modest. We’ve held 2 XCTDs in reserve for this phase (none were originally programmed). We’ll use the first in conjunction with a 3-depth spiral tonight and, if it works & we don’t need to launch a backup, use the final for another 3-depth tomorrow. There will also be some in-line samples in the vicinity of the Yermak. Commenced transit to the start point of the Yermak survey. |
| 0950 | Came shallow for brief housekeeping before starting Yermak survey. |
| 1054 | Completed housekeeping. Commenced Yermak Survey, Leg 1. This survey will consist of 11 boustrophedon legs oriented roughly 146/326 moving westward along the northeast tip of the Yermak Plateau. The first 2 legs will be in deep water east of the tip and will be about twice the length of subsequent legs. The survey will be done at 16kts/750ft. We’ll take in-line samples every 6 hours (nominally at 6/12/18/24) |
| 1201 | Commenced in-line samples (Event #239). |
| 1402 | Completed Leg 1. |
| 1424 | Commenced Leg 2. |
| 1730 | Completed Leg 2. |
| 1755 | Commenced Leg 3. |
| 1801 | Commenced in-line samples (Event #240). |
| 1930 | Completed Leg 3. Came shallow for brief housekeeping while repositioning. |
| 2005 | Completed housekeeping. |
| 2016 | Commenced Leg 4. |
| 2151 | Completed Leg 4. |
| 2213 | Commenced Leg 5. |
| 2347 | Completed Leg 5. |

# 13 May 1999

| 0001 | Commenced in-line samples (Event 241). |
| --- | --- |
| 0005 | Commenced Leg 6. |
| 0138 | Completed Leg 6. We’ll conduct our daily housekeeping and a 3-depth spiral during the repositioning. |
| 0141 | Launched XCTD #152. No data. We have kept one reserved for this contingency and will launch it now. |
| 0147 | Launched XCTD #153. Again, no data. That was our last one. |
| 0153 | Commenced 3-depth samples despite absence of any XCTD data here (Event #242). |
| 0225 | Completed samples. Proceeding with housekeeping. |
| 0546 | Completed housekeeping. |
| 0601 | Commenced in-line samples (Event #243). |
| 0604 | Commenced Leg 7. |
| 0738 | Completed Leg 7. |
| 0757 | Commenced Leg 8. |
| 0923 | Completed Leg 8. |
| 0942 | Commenced Leg 9. |
| 1110 | Completed Leg 9. |
| 1131 | Commenced Leg 10. |
| 1201 | Commenced in-line samples (Event #244). |
| 1250 | Completed Leg 10. |
| 1314 | Commenced Leg 11. |
| 1431 | Completed Yermak Survey. We will now transit westward then southward along the Yermak Plateau on our way out of the Arctic. During part of this, we’ll have to come shallow and slow because of the shallow depths over the Plateau. Later this afternoon, we’ll start looking for a site for our final surfacing. |
| 1436 | Came shallow for brief housekeeping. |
| 1505 | Completed housekeeping. |
| 1801 | Commenced in-line samples (Event #245). This was our final water sample event. |
| 1915 | Slowing to 14.5 kts and coming shallow to 310 ft while crossing shallow portions of the ridge. Keeping an eye out for a place to surface though we’d prefer to surface further south. The purpose of this surfacing is to get a final SINS/GPS tie for track reconstruction by the SCAMP people. We’d like this to be through-ice rather than open water or MIZ but are rapidly approaching the MIZ. |
| 2129 | Reversing course to investigate a large surfaceable feature we just passed. |
| 2137 | Coming shallow to improve our view of the ice. Within the last hour, the water has gotten much more turbid, another indication that we are approaching the MIZ. |
| 2204 | The feature we’ve been examining is open water with a lot of loose ice. Because a search further to the south would only take us into more MIZ-like conditions, we’re returning to the last good feature we saw, about 15nm to the northeast. |
| 2322 | Approaching last large thin-ice feature. Coming shallow & slowing to get a good initial look. |
| 2330 | This looks good. Commenced mapping. |

# 14 May 1999

| 0012 | Commenced ascent. |
| --- | --- |
| 0017 | Surfaced through 18” of soft ice. We’ll stay here for a couple hours getting fixes. |
| 0629 | Submerged. While on the surface, we switched back from transverse to geographic heading reference. |
| 0702 | Ready to go again. We’ll proceed to the egress point at 310ft/14.5kts. |
| 1400 | We’re within 10nm of the extended boundary of the Data Release Area. Turning east to parallel the boundary. |
| 1431 | Coming shallow for housekeeping. |
| 1539 | Completed housekeeping. |
| 1548 | We’ve decided to come shallow for one final fix before we depart. Since we’re in open water, we’ll go up to periscope depth – the first time we’ve done so in almost 2 months. |
| 1614 | At periscope depth. Proceeding south toward our egress point. |
| 1830 | Departed the Data Release Area. Completed scientific portion of the mission. |